## STM32 GRBL Port Notes

Macros:
#define TICKS_PER_MICROSECOND 168

stepper.c:

pwm/ocr/timsk registers: / st_wake_up() ↔ st_go_idle() / STEPPERS_DISABLE_PORT (macro) / TIMSK1 ← (enable stepper timer interrupt) / TCCR1B ← (set CS10/CS11/CS12: prescaler)	LL_TIM_EnableIT_UPDATE() / LL_GPIO_(Re)SetPin(GPIOx,GPIO_PIN_y) / LL_TIM_EnableCounter / TIM_Base_InitTypeDef::TIM_ClockDivision

ISR(TIMER1_COMPA): / set DIRECTION_PORT (macro) / set STEP_PORT using st.step_outbits / TCNT0 ← st.step_pulse_time / Start Timer0 / sei() : (resume interrupts) / grabbing a new segment: lines 352 – 402 / OCR1A ← (cycles per tick) / check if there is one: / initialize step segment timing (OCR1A) / if not, basically → shut down. / st_go_idle(): / TIMSK1 ← disable interrupt / TCCR1B ← reset timer/prescaling / ~ spin down spindle / → call to manage probing / <Bresenham> / ISR(TIMER0_OVF): l / STEP_PORT ← reset stepping pins (not dir pins) / TCCR0B ← stop the reset timer / st_reset(): / STEP_PORT ← initialize step and dir pins / DIRECTION_PORT ← etc / stepper_init(): / STEP_DDR |= STEP_MASK / STEPPERS_DISABLE_DDR |= 1<<STEPPERS_DISABLE_BIT / DIRECTION_DDR |= DIRECTION_MASK / TCCR1A/B ← (sets output compare / CTC mode) TCCR1A ← (disconnect output pins) / TIMSK0 &= ← (disconnect OC-INT and OVF-INT) / TCCR0A ← 0 (disconnected OC0A pin) / TCCR0B ← 0 (disconnected OC0B pin) / TIMSK0 |= (1<<TOIE0) (enable overflow interrupt)	NVIC handler at 0x000000b0 (TIM2) / LL_GPIO_(Re)SetPin(GPIOx,GPIO_PIN_y) / LL_GPIO_(Re)SetPin(GPIOx,GPIO_PIN_y) / LL_TIM_SetAutoReload(step_pulse_time) / or LL_TIM_EnableCounter / AVR: handlers start with itt disabled STM: handlers start with itt enabled / LL_TIM_OC_SetCompareCH1 / *note that it is preloaded by default / *will HAL try to write this reg again? / *if you set it in the handler, will it take effect immediately? Vs avr? / NVIC handler at 0x000000b4 (TIM3) / LL_GPIO_ClearPin(GPIOx,GPIO_PIN_y) / LL_TIM_DisableCounter / LL_GPIO_SetPin(GPIOx,GPIO_PIN_y) / LL_GPIO_SetPin(GPIOx,GPIO_PIN_y) / LL_GPIO_SetPin(….) / L_GPIO_SetPinMode(*,LL_GPIO_MODE_OUTPUT) LL_TIM_OC_SetMode() / TIM2_CCMR1 &= ~(TIM_CCMR1_OC1M_Msk) / TIM2_DIER &= ~(1<<TIM_DIER_UIE) / TIM2_DIER |= (1<<TIM_DIER_UIE)

cpu_map.h:
* should crosslink a separate file that manages the pin mapping
This will likely lead to the schematic for the expansion shield

whole file is ports and pins	See if the port/pin syntax is directly transferable to STM32HAL. If not, we’ll be making a stm32_map.h and excluding this file.

nuts_bolts.c:

_delay_us() / _delay_ms()	There’s spin-delay functionality in the cube pkg under a Utils directory

serial.c:

serial_init(): / set baud, tx&rx, data rdy interrupt	There’s an STM32 USB library that will be needed to speak with the host machine. We need to implement the serial device interface and write routines for serial_init, serial_write, serial_read, the SERIAL_UDRE(tx) and SERIAL_RX(rx) interrupt handlers. / So this might require a separate serial_stm32.c that will replace certain symbols.

eeprom.c:

eeprom_get_char() and eeprom_put_char() / EEAR / EECR / EERE / EEDR

## Newly added files

The folder stm32f407/ holds a bunch of git submodules. These are firmware and middleware packages from the official STMicro github for the STM32F4xx device family.

If you wanted to port to a separate microcontroller, you could feasibly just add the appropriate git submodules and clone or edit the Makefile.stm32 file so that it reads from those alternate directories for stm32-related code.

There are three major submodules that you’ll need: CMSIS firmware, HAL drivers, and the USB middleware.

### CMSIS
CMSIS has some subfolders, arm/gcc/iar or some such. This project is compiled with gcc, so folders and source come from this location.

### Interrupt Priority
The grbl code might be ensuring that its stepper pulse timer has higher interrupt priority, or it might inherit a certain level of priority over other interrupts due to avr architecture and/or avr defaults. Ensure that the STM32 implementation assigns adequate priority to the pulse timer so that these pulses are are produced with consistent timing.
STM32 Pin assignments

TIM2: Timer encoder capture (3 channels)
TIM2_CH1 ↔